## Slide 1: Verification and Synthesis of Control Barrier Functions
Paper Reading

## Slide 2: Motivation
The problem of verifying whether the CBF constraints can always be satisfied has received less attention. The work propose a framework for verifying that a CBF guarantees safety for all time and synthesizing CBFs with verifiable safety in polynomial control systems.
The approach is based on the fact that the safety guarantees rely on two properties.
  There should be no point on the boundary of the CBF for which the Lie derivative of the CBF is always negative
  The safe region of the CBF should be contained within the overall safe region.

## Slide 3: Contribution
The paper develop a SOS program for verifying that a given CBF construction ensures safety. We extend this approach to high-order CBFs and systems with multiple CBF constraints.
The paper propose an alternating-descent heuristic for synthesizing CBFs using the proposed conditions.
Considering special cases of the approach, including compact safe regions and constraints where the unsafe region is a union of non-overlapping convex sets.

## Slide 4: CBF Verification
Consider a nonlinear dynamic control system with dynamic:
where denotes the state, is a control input, and and are polynomials. The safe region is defined as , where is a polynomial. The boundary of the safe region, denoted , is defined by . The viability kernel is defined as:
Definition 1: The viability kernel is a set such that, for any , there is a control input signal that guarantees for all time when the initial state is

## Slide 5: CBF Verification
Problem 1: Given a system (1) and a safety constraint set , (i) verify whether a set is contained in the viability kernel, and (ii) verify that a given control policy ensures that the system state remains in the viability kernel.
Note that we do not consider any constraints on the control input (e.g., limits on actuation).
Definition 2: A function is a control barrier function for system (1) if there is a class-K function such that, for all with , there exist satisfying

## Slide 6: CBF Verification
Theorem 1: A polynomial is a CBF for (1) if and only if there exist polynomials SOS polynomials and , and an integer such that:
Moreover, the set is a subset of the viability kernel of if (3) holds and there exist SOS polynomials and and a polynomial such that
Proposition 1: The function is a CBF iff there is no satisfying .

## Slide 7: Control Barrier Function Construction
Problem 2: Given a system (1) and a safety constraint set , construct a CBF that verifiably guarantees positive invariance of .
We initialize arbitrarily and parameters and to be infinite. At step , we solve the following SOS program with variable and
s.t.

## Slide 8: Control Barrier Function Construction
is a fixed SOS polynomial of sufficiently large degree to ensure that the first constraint is SOS for sufficiently large . We let denote the value of returned by the optimization. The procedure terminates if or if . Otherwise, we solve the SOS problem with variables and given by
s.t.
denote the value of returned by the optimization. The procedure terminates if or if .

## Slide 9: Compact Safe Region
Lemma 1: Let satisfy and . Then there exist a positive definite matrix and such that the function
is a CBF with .
Lemma 2: If is a CBF, then the set
is in the viability kernel.
Unsafe Region
Safe Region

## Slide 10: Compact Safe Region
Theorem 9: Suppose that is a fixed point of (1), P is a solution to the Lyapunov equation corresponding to a stabilizing controller of the linearized system, and the SOS constraints
and
hold for some polynomials and SOS polynomials and . Then is a CBF and is in the viability kernel.

## Slide 11: Compact Unsafe Region
We consider a special case where the viability kernel and are identical. This is the case of controllable linear systems where the safe region is given by , where each is a convex function, and the distance for all and .
Theorem 10: Under the conditions described above, the viability kernel is equal to , and there exists a CBF-based policy that ensures safety.
Safe Region
UnSafe Region

## Slide 12: Simulation